## Slide 2: COMPACTION
Topic
COMPACTION
Presented to
Dr. Ayub Elahi
Presented by Group leader.
M.Zeeshan haider yousaf Zia. # 14
Haider ayub # 13
Bilal ansari #35

## Slide 3: COMPACTION

## Slide 4: COMPACTION
Definition
Compaction is a process that brings about an increase in soil density or unit weight, accompanied by a decrease in air volume. There is usually no change in water content.

## Slide 5: COMPACTION
process by which the porosity of a given form of sediment is decrease as a result of its mineral grains being squeezed together by the weight of overlying sediment or by mechanical means.

## Slide 6: COMPACTION
Types of compaction
  Soil compaction
  Dynamic compaction
  Waste compaction
  Data compaction
  Cold compaction
  Powder compaction

## Slide 7: COMPACTION
Powder compaction
  Redirect from cold
  Many equipment used
  Also known is powder pressing
  Three major stages for fabrication techniques
  First primary material is physical powdered divided into small individual particles

## Slide 8: COMPACTION
Dynamic compaction
  To increase the density of soil

## Slide 9: COMPACTION
Methods of compacting concrete.
Hand Compaction
  Rodding
  Ramming
  Tamping

## Slide 10: COMPACTION
Compaction by Vibration
  Internal vibrator (Needle vibrator)
  Formwork vibrator (External vibrator)
  Table vibrator
  Platform vibrator
  Surface vibrator (Screed vibrator)
  Vibratory Roller

## Slide 11: COMPACTION
Types of compaction plant
  Smooth-wheeled roller
  Grid roller
  Sheep foot roller
  Pneumatic-tyread roller
  Vibrating plate
  Power rammer

## Slide 12: COMPACTION
Smooth-wheeled roller
  Self-propelled or towed steel rollers ranging from 2 - 20 tones
  Suitable for: well-graded
  sands and gravels silts and clays of low
  plasticity
  Unsuitable for: uniform
  sands; silty sands; soft clays

## Slide 13: COMPACTION
Grid roller
  Towed units with rolls of 30-50 mm bars, with spaces between of 90-100 mm
  Masses range from 5-12 tones
  Suitable for: well-graded sands; soft rocks; stony soils with fine fractions
  Unsuitable for: uniform sands; salty sands; very soft clays

## Slide 14: COMPACTION
Sheep foot roller
  Also known as a 'tamping roller'
  Self propelled or towed units, with hollow drum fitted with projecting club-
  shaped 'feet'
  Mass range from 5-8 tones
  Suitable for: fine grained
  soils; sands and gravels,
  with >20% fines
  Unsuitable for: very coarse soils; uniform gravels

## Slide 15: COMPACTION
Pneumatic-tyred roller
  Usually a container on two axles, with rubber-tyred wheels.
  Wheels aligned to give
  a full-width rolled track.
  Dead loads are added to
  give masses of 12-40 tones.
  Suitable for: most coarse and fine soils.
  Unsuitable for: very soft clay; highly variable soils.

## Slide 16: COMPACTION
Vibrating plate
  Range from hand-guided machines to larger roller combinations
  Suitable for: most soils
  with low to moderate
  fines content
  Unsuitable for: large
  volume work; wet clayey
  soils

## Slide 17: COMPACTION
Power rammer
  Also called a 'trench tamper'
  Hand-guided pneumatic tamper
  Suitable for: trench
  back-fill; work in confined
  areas
  Unsuitable for: large volume
  work

## Slide 18: COMPACTION
Compaction techniques
Compaction is attained by applying energy to a soil by the following methods:
  Kneading
  Static weight
  Vibration
  Impact
  Explosives

## Slide 19: COMPACTION
Vibration
vibration is generally accept as an economical, labor saving and quality improving method of compaction, which is used in must of concrete jobs. It is especially adapted to the stiffer consistencies associated with high quality conceit.

## Slide 20: COMPACTION
Compaction as a construction process
Compaction is employed in the construction of road bases, runways, earth dams, embankments and reinforced earth walls. In some cases, compaction may be used to prepare a level surface for building construction.
Soil is placed in layers, typically 75 mm to 450 mm thick. Each layer is compacted to a specified standard using rollers, vibrators or rammers.

## Slide 21: COMPACTION
Objectives of compaction
Compaction can be applied to improve the properties of an existing soil or in the process of placing fill. The main objectives are to:
increase shear strength and therefore bearing capacity
increase stiffness and therefore reduce future settlement
decrease voids ratio and so permeability, thus reducing potential frost heave .

## Slide 22: COMPACTION
Factors affecting compaction
A number of factors will affect the degree of compaction that can be achieved:
Nature and type of soil, i.e. sand or clay, grading, plasticity .
Water content at the time of compaction .
Site conditions, e.g. weather, type of site, layer thickness
Compactive effort: type of plant (weight, vibration, number of passes) .

## Slide 23: COMPACTION
Effect of increased compactive effort
The compactive effort will be greater when using a heavier roller on site or a heavier rammer in the laboratory. With greater compactive effort:
maximum dry density increases
optimum water content decreases
air-voids content remains almost the same.

## Slide 24: COMPACTION
Effect of soil type
Well-graded granular soils can be compacted to higher densities than uniform or silty soils.
Clays of high plasticity may have water contents over 30% and achieve similar densities (and therefore strengths) to those of lower plasticity with water contents below 20%.
As the % of fines and the plasticity of a soil increses, the compaction curve becomes flatter and therefore less sensitive to moisture content. Equally, the maximum dry density will be relatively low.

## Slide 25
  The End
Thanks