## Slide 1
Roll No.
14, 23, 25, 29, 43
EFFECT OF EARTHQUAKE LOADING ON MULTI-STORY BUILDINGS AND THEIR REMEDY

## Slide 2: EARTHQUAKE
An earthquake (also known as a quake, tremor or temblor) is the result of a sudden release of energy in the Earth crust that creates Seismic waves.

## Slide 3: Classifications and causes of Earthquake
Tectonic Earthquakes
Non-Tectonic Earthquakes

## Slide 4: Earthquake Phenomenon

## Slide 5: Types of Waves
  -Body waves travel through the body of the material (1/R2 fall-off: energy distributed on sphere)
    P-waves are compressional waves, like sound in air and are the fastest.
    S-waves are vibrations at right angles to the direction of propagation, like light, and are second fastest.
  Surface waves travel along an interface, as between air and ground, or loose materials and bedrock and cause most of the damage in earthquakes. (1/R fall-off: energy distributed on circle)
    Rayleigh waves travel along the rock-air interface, and cause the most damage and are like water waves
    Love waves are transverse and travel along solid-solid boundaries, like bedrock.

## Slide 6: Earthquake force
Force due to earthquake is
  (Seismic Coefficient)
  W = Weight of structure;
  g = Acceleration due to gravity;
  a = peak earthquake acceleration.
  IS:1893-1984 provides the general principles and design criteria for earthquake loads

## Slide 7
Effect of Earthquake
House Elements Resist Horizontal Forces
(Before Earthquake)
(After Earthquake)
Shear Wall
Cripple Wall
Foundation
Floor
Diaphragm
Roof Diaphragm
f1
f2
f3
fsum = f1 + f2 + f3

## Slide 8
What happens to the buildings?
If the ground moves rapidly back and forth, then the foundations of the building are forced to follow these movements. The upper part of the building however «would prefer» to remain where it is because of its mass of inertia. This causes strong vibrations of the structure with resonance phenomena between the structure and the ground, and thus large internal forces. This frequently results in plastic deformation of the structure and substantial damage with local failures and, in extreme cases, collapse.

## Slide 9: SEISMIC LOADING
Seismic loading is one of the basic concepts of Earthquake Engineering which means application of an earthquake-generated agitation to a structure. It happens at contact surfaces of a structure either with the ground, or with adjacent structures , or with gravity waves from Tsunami.

## Slide 11
Buildings with First-Soft Storey
Soft storey attracts large earthquake force and requires very large ductility. To make stiffness of the ground storey, comparable with that of the upper storey's large column and beam sizes and / or shear walls have to be provided.
In absence of detailed non linear dynamic analysis, the ground storey should be designed for 2.5 times the storey shear and moment obtained from the analysis of bare frame.

## Slide 12: Buildings with Heavy Water Tanks

## Slide 13
EARTHQUAKE ANALYSIS
x
m
SDOF system(Single degree of freedom)

## Slide 14
EQUATION OF MOTION
m
kx
Free Body Diagram
Governing Equation

## Slide 15
(a) MDOF system
m1
m2
mN
k1
kN
k2
(b) Free body diagram
mi
MDOF System
Figure 2.4

## Slide 16: Distribution of earthquake forces in multi-story building

## Slide 17: Condition assessment
Tapping by hammer
Rebound Hammer
Indentation method
Ultrasonic Pulse Velocity Transmission Test
Covermeter / Pachometer
Radiography
Chloride Content
Testing for Depth of Carbonation
Tests on Concrete Cores

## Slide 18
New stirrups
New reinforcement
Old reinforcement
Roughened surface
Drilled hole in slab
Roughened surface
Slab
Stirrups
Beam
Jacket
Strengthening of column

## Slide 19
New stirrups
New reinforcement
Old reinforcement
Anchor bars
Drilled hole in slab
New reinforcement
Old reinforcement
New stirrups
Strengthening of column

## Slide 20
weld
Roughened surface
New reinforcement
Beam Strengthening

## Slide 21
Strengthening of bare frame

## Slide 22
Strengthening of masonry

## Slide 23
Diagonal Bracing

## Slide 26
Non-isolated
Base-isolated

## Slide 27
Fixed base building Base-isolated building

## Slide 28
SEISMIC BASE ISOLATION
g
x
&
&
1
x
2
x
N
x
m
1
m
2
m
N
k
1
k
N
k
2
m
b
Base isolator

## Slide 29: Elastomeric bearings

## Slide 30: Sliding bearings

## Slide 31
36
110
6
1.5
30
Steel Plate
Rubber
12
12

## Slide 33
THANK YOU